## Slide 1
Lecture 2
Operational Amplifier:
Introduction, Open Loop Configuration, Closed Loop Introduction

## Slide 2: Operational Amplifiers
Textbook

## Slide 3: Outline
Operational Amplifier: Introduction
  - Dependent Sources
  - Op-Amp: Circuit Symbols and terminal
  - Op-Amp: VTC (Voltage Transfer Characteristics)
    Linear Amplification
    (Positive and Negative) Saturation
  - Op-Amp: Examples
  - Op-Amp: Physical Entity

## Slide 4: Dependent Sources
To analyze op-amps, we must understand dependent source.
A dependent source generates a voltage or current whose value depends on another voltage or current.
Example: current-controlled current source

## Slide 5: Dependent Sources
Voltage Gain:

## Slide 6: Dependent Sources
Dependent sources are two-ports: characterized by two equations.
Here and .
Resistors, (Ind.) Voltage sources, (Ind.) Current sources are single “port” device. They are characterized by a single equation.

## Slide 7: Operational Amplifier: Introduction
Operational:
Mathematical Operations
Amplifier:
Amplifies input signal/voltage.
Small Signal
Large Signal
=
Small Signal
Large Signal
An op-amp (operational amplifier) can be modelled by a voltage- controlled voltage source.

## Slide 8: Operational Amplifier: Introduction
=
Small Signal
Large Signal
An op-amp (operational amplifier) can be represented by a voltage- controlled voltage source.
and where is large (typically ).

## Slide 9: Op-Amp: Circuit Symbols and terminal
Inverting terminal voltage
Non-inverting terminal voltage
Positive Saturation / Supply Voltage
Negative Saturation / Supply Voltage
Output Voltage

## Slide 10: Op-Amp: Circuit Symbols and terminal
 | Differential input voltage
 | Differential input voltage
Voltage Transfer Characteristics (VTC)
Difference Amplifier –
  Amplifies the voltage difference between two terminals.
=

## Slide 11: Op-Amp: VTC – Linear Amplification
Voltage Transfer Characteristics (VTC)
- Shows how the output voltage varies with the input voltage
- axis
- axis
- Slope:
No amplification
Attenuation
Amplification
If the line passes through origin:
LINEAR AMPLIFICATION
15 V
1.5 V

## Slide 12: Op-Amp: VTC – Linear Amplification
Linear Amplification only takes place within a valid input range.
Otherwise output will be distorted - - Saturation
The limiting factor of linear amplification is determined by the power supply to the amplifier

## Slide 13: Op-Amp: VTC - Saturation
Amplification factor
If Positive Saturation
If Negative Saturation
: When
: Gain / Amplification
Non-Linear characteristics

## Slide 14: Op-Amp: VTC - Saturation
Amplification factor

## Slide 15: Op-Amp: VTC - Summary
If Positive
If Negative
Output
axis
Input
axis
Voltage Transfer Characteristics (VTC)
Linear Region
: When is very small
Positive saturation:
Negative saturation:

## Slide 16: Op-Amp: Examples
Find

## Slide 17: Example 1
Solution:
Since

## Slide 18: Example 2
Solution:
Since
(Negative saturation)

## Slide 19: Op-Amp: Physical Entity
Circuit symbol for the general-purpose op amp.
Pin numbering is that for an 8-pin mini-DIP package
NC – No Connection
A-741C
Difference Amplifier – Amplifies the voltage difference between two terminals.
2
3
7
4
6
Manufacturer ID
Part Identification Number (PIN)
C: Commercial ()
I: Industrial ()
M: Military ()

## Slide 20: Op-Amp: Summary
Op-Amp Amplifies the difference between the voltages at it’s two input terminals -
However, the Amplification is limited within voltage levels defined by the positive and negative saturation voltages .
The “ideal” op-amp behaves like a voltage dependent voltage source within the linear region.

## Slide 21: Thank you!
Part 1 ends here

## Slide 22: Outline
Op-Amp: Open Loop Configuration
  Op-Amp: Circuit Modelling
  Example Problem – Op-amp model
  Op-amp configuration – open and closed loop
  Open Loop op-amp: Voltage Transfer Characteristics
  Open Loop op-amp: Comparators

## Slide 23: Op-Amp (Recap)
Operational:
Mathematical Operations
Amplifier:
Amplifies input signal/voltage.
Small Signal
Large Signal
=
Small Signal
Large Signal
An op-amp (operational amplifier) can be represented by a voltage- controlled voltage source.

## Slide 24: Op-Amp: VTC (Recap)
If Positive
If Negative
Voltage Transfer Characteristics (VTC)
Linear Region
: When is very small
Positive saturation:
Negative saturation:

## Slide 25: Op-Amp: Circuit Modelling
Voltage controlled voltage Source
“Ideal” op-amp approximation

## Slide 26: Op-amp: Circuit Model and VTC
Voltage (Differential/OL) Gain: or
Positive Saturation Voltage:
Negative Saturation Voltage:
Parameter | Typical Range | Ideally
Parameter | Typical Range | Ideally
Slope of VTC
Input
axis

## Slide 27: Op-amp: Circuit Model and VTC
Voltage Transfer Characteristics (VTC)
Linear Region
Positive saturation:
Negative saturation:
: Open Loop Gain

## Slide 28: Types of Op-Amp configuration
Open loop configuration:
  No physical connection between input and output
Closed loop configuration:
  Feedback from output terminal

## Slide 29: Open Loop Configuration: Comparator
Level Crossing Detector / Comparator
NON-INVERTING COMPARATOR

## Slide 30: Open Loop Configuration: Comparator
Level Crossing Detector / Comparator
INVERTING COMPARATOR

## Slide 31: Open Loop Configuration: Comparator
INVERSE RELATIONSHIP!
Increases
Decreases
INVERTING COMPARATOR VTC!
Downward step (Staircase)
Input in Inverting terminal

## Slide 32: Open Loop Configuration: Comparator
NON-INVERTING
(INCREASING)
RELATIONSHIP!
Increases
Increases
NON-INVERTING COMPARATOR!
Upward step (Staircase)
Input in Non-Inverting terminal

## Slide 33: Open Loop Configuration: Comparator
Zero Crossing Detector
Compare values with a reference and pin value to if voltage is above or to below that.
Non-inverting configuration

## Slide 34: Open Loop Configuration: Comparator
Zero Crossing Detector
Inverting configuration

## Slide 35: Summary
Level Crossing Detector / Comparator

## Slide 36
Part 2 ends here

## Slide 37: Outline
Op-Amp: Comparator
  Open Loop Configuration: Example 1
  Open Loop Configuration: Example 2
  Open Loop Configuration: Example 3

## Slide 38: Open Loop Configuration: Example 1
Design a circuit using op-amp that has the voltage transfer characteristics as shown in the figure below. is the output voltage and is the input voltage.
Solution:
Inverting comparator

## Slide 39: Open Loop Configuration: Example 2
Draw the voltage transfer characteristic (VTC) curve ( vs ) from the adjacent waveform graph. Also draw the Op-Amp Circuit that would give rise to such a VTC.
smaller than  Positive Saturation
larger than  Negative Saturation
INVERTING CONFIGURATION
Solution:

## Slide 40: Open Loop Configuration: Example 3
Design an op-amp circuit to transform the sinusoidal voltage, ( is in units of , and time-period is ), to: A square wave with a duty cycle of 25%.
Solution:

## Slide 41: Open Loop Configuration: Example 3
Design an op-amp circuit to transform the sinusoidal voltage, ( is in units of , and time-period is ), to: A square wave with a duty cycle of 25%.
Solution:

## Slide 42: Open Loop Configuration: Example 3
Design an op-amp circuit to transform the sinusoidal voltage, ( is in units of , and time-period is ), to: A square wave with a duty cycle of 25%.
Solution:
Positive Saturation
Negative Saturation
NON-INVERTING CONFIGURATION

## Slide 43: Open Loop Configuration: Example 3
Design an op-amp circuit to transform the sinusoidal voltage, ( is in units of , and time-period is ), to: A square wave with a duty cycle of 25%.

## Slide 44
Part 3 ends here

## Slide 45: Outline
Comparator Application - Smoke Detectors
Smoke Detector – Operation
Comparator Application – Automatic AC
General Principle - Comparator

## Slide 46: Comparator Application - Smoke Detectors
Working Principle:
Smoke present Alarm rings
No smoke present No Alarm rings.
Smoke levels Voltage
Since the alarm is an electrically driven device, we need some method to convert smoke levels to proportionate voltage.

## Slide 47: Comparator Application - Smoke Detectors
Voltage Divider
Op-Amp comparator
LED Circuit

## Slide 48: Smoke Detector - Operation
Light from the LED is reflected off the smoke particles on to the photoconductor –
Light Dependent Resistor (LDR).
No Smoke
No scattering
Low intensity at LDR (Dark - )
Smoke Present
High scattering from smoke particles
High intensity at LDR (Light - )
LED Circuit
Voltage Divider
LDR @
Light is lost in the environment

## Slide 49: Smoke Detector - Operation
No Smoke
No scattering
Low intensity at LDR (Dark - )
High resistance across LDR ()
Smoke Present
High scattering from smoke particles
High intensity at LDR (Light - )
Low resistance across LDR ()
Voltage Divider
LDR @
Light is lost in the environment

## Slide 50: Smoke Detector - Operation
No Smoke
No scattering
Low intensity at LDR (Dark - )
High resistance across LDR ()
Decrease in
Smoke Present
High scattering from smoke particles
High intensity at LDR (Light - )
Low resistance across LDR ()
Increase in
Voltage Divider

## Slide 51: Smoke Detector - Operation
No Smoke
No scattering
Low intensity at LDR (Dark - )
High resistance across LDR ()
Decrease in
Possibility of
Smoke Present
High scattering from smoke particles
High intensity at LDR (Light - )
Low resistance across LDR ()
Increase in
Possibility of
Non-inverting Op-Amp comparator

## Slide 52: Smoke Detector - Operation
Voltage Divider
Non-inverting Op-Amp comparator
LED Circuit
Scattering on to LDR Bright - Positive saturation

## Slide 53: Smoke Detector - Operation
Voltage Divider
Non-inverting Op-Amp comparator
LED Circuit
Scattering on to LDR Bright - Positive saturation

## Slide 54: Comparator Application – Automatic AC
Off
AC
Temperature
Temperature Sensor
Sensitivity control
Comparators can be used to switch on an AC based on a Temperature.
  Temp. AC - ON
  Temp. AC – OFF
  Temp
The sensitivity of switching on the AC is determined by
On
NON-INVERTING RELATIONSHIP: NON INVERTING COMPARATOR

## Slide 55: Comparator Application – Summary
Off
Device
Physical Quantity
Sensor
Sensitivity control
Comparators can be used to switch on any device based on a Physical Quantity.
  Phys. Qnty. DEVICE – ON / OFF
  Phys. Qnty. DEVICE – OFF / ON
  Phys. Qnty.
The sensitivity of switching on the AC is determined by
On
This Relationship:
Determines the type of Comparator

## Slide 56: Solving Comparator Problems
Determine type of comparator from the relationship.
Determine from the switching condition from the provided information
Determine the saturation voltages from the output device
Off
Device
Physical Quantity
Sensor
On

## Slide 57
Part 4 ends here

## Slide 58: Outline
Operational Amplifier: Non-ideal Circuit Modelling
  - Ideal VS Non-Ideal Model
  - Op-Amp: Circuit Symbols and terminal
  - Op-Amp: VTC (Voltage Transfer Characteristics)
    Linear Amplification
    (Positive and Negative) Saturation
  - Op-Amp: Examples
  - Op-Amp: Physical Entity

## Slide 59: Op-Amp: Circuit Modelling
Voltage controlled voltage Source
“Ideal” op-amp approximation
“Non-Ideal” op-amp approximation
-
+

## Slide 60: Op-amp Model parameters
-
+
Input resistance:
Output resistance:
Voltage (Differential/OL) Gain: or
Positive Saturation Voltage:
Negative Saturation Voltage:
Parameter | Typical Range | Ideally
Parameter | Typical Range | Ideally
Slope of VTC
Output
axis
Input
axis

## Slide 61: Practice Problem – op-amp
Find and .
Here,

## Slide 62: Practice Problem – op-amp
KCL at node
KCL at node
Find and .
Here,

## Slide 63: Some circuits with OP-AMP
Find and .
Here,
5
40

## Slide 64
Part 5 ends here

## Slide 65: Closed Loop Configuration
Feedback

## Slide 66: Outline
Feedback in Op-Amp circuit
Negative Feedback
Open Loop VS Closed Loop Gain
Closed Loop Configuration

## Slide 67: Feedback in Op-Amp circuit
Two types of feedback
  Negative Feedback:
    Output voltage is fed to the inputs negatively
    The output voltage is connected to the inverting terminal
  Positive Feedback:
    Output voltage is fed to the inputs positively
    The output voltage is connected to the non-inverting terminal

## Slide 68: Feedback in Op-Amp circuit
Two types of feedback
  Negative Feedback:
    Output voltage is fed to the inputs negatively
    The output voltage is connected to the inverting terminal
  Positive Feedback:
    Output voltage is fed to the inputs positively
    The output voltage is connected to the non-inverting terminal

## Slide 69: Negative Feedback in Op-Amp circuit
Negative Feedback:
  Output voltage is fed to the inputs negatively
  The output voltage is connected to the inverting terminal
Here,
We know,
If then .
This is the new amplification factor / Gain

## Slide 70: Open Loop Gain VS Closed Loop Gain
With “Negative Feedback”: Closed Loop (CL) Configuration
Input Voltage:
Output Voltage:
Open Loop (OL) Configuration
Input Voltage:
Output Voltage:
OL Gain | CL Gain
OL Gain | CL Gain

## Slide 71: Open Loop Gain VS Closed Loop Gain
Closed Loop (CL) Configuration
Open Loop (OL) Configuration
OL Gain | CL Gain
Can’t be controlled | Can be controlled by the feedback element
Used as “Comparator” | Used as “Linear Amplifier”
OL Gain | CL Gain
Can’t be controlled | Can be controlled by the feedback element
Used as “Comparator” | Used as “Linear Amplifier”

## Slide 72: Negative Feedback in Op-Amp circuit
The output voltage is transformed in the following way:
This factor of can be achieved with a voltage divider network.
A voltage divider can act as a multiplier/factor in the feedback branch

## Slide 73: Negative Feedback in Op-Amp circuit
A voltage divider can act as a multiplier/factor in the feedback branch
If = 10 (meaning we feed back one tenth of the output to negative input), we will get =10*. that is 10-fold gain.

## Slide 74: Solving Closed Loop Op-Amp Circuit
For “ideal” op-amp
  Infinite input resistance,
  Zero output resistance,
  and
When there is negative feedback,
  In an ideal op-amp, “” (or ) is infinitely high. Thus, for a finite output voltage
  .
  This is called virtual short circuit