## Slide 1: CSE251: Electronic Devices and Circuits
Prepared By:
Shadman Shahid (SHD)
Lecturer, Department of Computer Science and Engineering, School of Data and Sciences, BRAC University
Email: ext.shadman.shahid@bracu.ac.bd
Lecture: 14 - 16 – MOSFET

## Slide 2: Outline
Introduction to Electronic Switches
Basic Inverter
Introduction to Controlled Sources
Introduction to MOSFET
MOSFET as digital switch
Designing Logic gates with MOSFETs

## Slide 3: Two terminal Devices
Voltage Source
Resistor
Current Source
Diode
Linear Devices
Non-linear Devices
Actual IV
PWL IV
PWL: Piecewise Linear
IV characteristics of two terminal devices are fixed.
IV characteristics of three terminal devices can be changed

## Slide 4: Three terminal Devices
IV of two terminal can be controlled using a third terminal.
Example: Switch, MOSFET, BJT
Switch
Switch ON
Switch OFF
IV characteristics between and can be controlled by
Control Signal (Physical/Voltage/Current)

## Slide 5: Switch – Types
Depending on the control, the switch can be
  Analog: Controlled using physical toggle/button
  Digital: Controlled using voltage or current. Example – MOSFET (voltage controlled), BJT (current controlled)
Analog switches
Digital switches (Transistors)

## Slide 6: Digital Representation
Memristor
Diode
Binary → Two states (0/False, 1/True)
Binary variables in circuit, need to use two states of device/parameters
Voltage |  | Current |  |  |  | State | 
5V  | 1 |  | 2mA |  | 1 | ON  | 1
0V  | 0 |  | 3mA |  | 0 | OFF  | 0
0V  1 3.3V  0 |  |  |  |  |  | Low resistance High resistance | 
 1
 0
We use this convention usually

## Slide 7: Switch Application – Logic Gates
We can use switches to build logic gates
A | B | Bulb
0 | 0 | OFF
0 | 1 | ON
1 | 0 | ON
1 | 1 | ON
A | B | Bulb
0 | 0 | OFF
0 | 1 | OFF
1 | 0 | OFF
1 | 1 | ON
AND operation
OR operation

## Slide 8: Switch Application – Logic Gates
A | Bulb
0 | ON
1 | OFF
A | B | Bulb
0 | 0 | ON
0 | 1 | ON
1 | 0 | ON
1 | 1 | OFF
A | B | Bulb
0 | 0 | ON
0 | 1 | OFF
1 | 0 | OFF
1 | 1 | OFF
NOT operation NAND operation NOR operation
These circuits are “preferred” – because they can be cascaded to build combinational logic circuits
-> if we remove the bulb and use the voltage across instead to cascade and drive the next gate

## Slide 9
Alternative representations:
Switch Application – Logic Gates

## Slide 10: Switch Application – Logic Gates
Alternative representations:

## Slide 11: Switch Application – Logic Gates
𝐴 | 𝑩 | 𝑉𝑶𝑼𝑻
0 | 0 | 5V
0 | 1 | 5V
1 | 0 | 5V
1 | 1 | 0V
𝐴 | 𝑩 | 𝑉𝑶𝑼𝑻
0 | 0 | 5V
0 | 1 | 0V
1 | 0 | 0V
1 | 1 | 0V
𝐴 | 𝑉𝑶𝑼𝑻
0 | 5V
1 | 0V

## Slide 12: Examples

## Slide 13
Implement using switches: 𝑓 = (𝐴 + 𝐵)𝐶
Example

## Slide 14
Practice Problem 1
In digital systems, binary data may be subjected to noise that can alter a 0 to a 1 or a 1 to a 0.
A simple way to check if any error has occurred is to use an even parity checker. If there are two input bits and , the output of the even parity checker (denoted as ) will be HIGH if there are even number of 1s, i.e., if both x and y are 0 or if both of them are 1.
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 15: Digital Representation
Suppose you want to send 010110
Single value based representaion fails in the presence of noise
Better approach – threshold-based system
Simplest: Logical 0 Logical 1

## Slide 16: Static Discipline
Specification for “all” digital devices
Requires devices to adhere to common representation to ensure that
valid input produces valid output
This means, if
  Sender sends “0” Receiver interprets as “0”
Sender sends ”1”
Receiver interprets as “1”

## Slide 17: Static Discipline
Naïve approach: Single threshold-based system
Valid 1
Valid 0
5V
0V
1
0
1
0
2.5V
sender
receiver
sender
Logical 0:
Logical 1:
receiver
Logical 0:
Logical 1:
What if ? It is undefined!
Channel
Device/Gate
Device/Gate

## Slide 18: Static Discipline
Double threshold based system
5V
0V
1
0
1
0
3V
sender
receiver
= High voltage threshold = 3𝑉
Valid 1
Forbidden Region
Valid 0
2V
What if 1.9𝑉 and channel noise is 0.5𝑉?
= 1.9𝑉 + 0.5𝑉 = 2.4𝑉 = invalid
 valid output producing invalid input, i.e., no margin for noise
sender
Logical 0:
Logical 1:
receiver
Logical 0:
Logical 1:
= High voltage threshold = 2 𝑉
Channel
Device/Gate
Device/Gate

## Slide 19: Static Discipline
Four threshold-based system  Tighter restriction on sender (output)
5V
0V
1
0
sender
receiver
Valid 1
NM1
Forbidden Region
NM0
Valid 0
= Output high voltage threshold = 4.5𝑉
= Output low voltage threshold = 0.5𝑉
= Input high voltage threshold = 3𝑉
= Input low voltage threshold = 2𝑉
1
0
2V
0.5V
4.5V
3V
Noise margins (NM):
(significance?)
(significance? )
For static discipline,
sender
Logical 0:
Logical 1:
receiver
Logical 0:
Logical 1:
Channel
Device/Gate
Device/Gate

## Slide 20
Static Discipline
Four threshold-based system  Tighter restriction on sender (output)
The lowest output voltage value that a digital device can produce when it outputs a logical 1.
The highest output voltage value that a digital device can produce when it outputs a logical 0.
The lowest input voltage value that a digital device must recognize as a logical 1.
The highest input voltage value that a digital device must recognize as a logical 0.

## Slide 21
Static Discipline and VTC graph
Four threshold-based system  Tighter restriction on sender (output)
During high to low or low to high transition:
While not in transition; at logical HIGH or LOW voltage level:
Higher Slope in VTC graph
Smaller Slope in VTC graph

## Slide 22
During high to low or low to high transition:
While not in transition; at logical HIGH or LOW voltage level:
Slope
Slope
Slope
Forbidden
Region
Forbidden
Region
Static Discipline and VTC graph

## Slide 23: Transistors as Digital Switch
Transistors are 3 terminal non-linear devices, can be used as switch
2 types – Voltage Controlled, Current Controlled
Metal Oxide Semiconductor Field Effect Transistor (MOSFET) are voltage controlled
Control, . The IV characteristics ( vs ) depends on
Actual dependency is complex.
Will start with a simple (but approximate) one – S-Model (Switch Model)

## Slide 24: MOSFET S-Model
The MOSFET (approximately) behaves like a switch
. Here, , and

## Slide 25: MOSFET S-Model

## Slide 26: Logic Gates using MOSFET
Just replace the switches with MOSFETs!
NOT Gate (Inverter)
NAND Gate (Inverter)
NOR Gate (Inverter)

## Slide 27: MOSFET Logic Gates – More Examples
𝑂𝑈𝑇 = 𝐴𝐵 + 𝐶 + 𝐷
𝑂𝑢𝑡 =
𝐴 + 𝐵 𝐶𝐷 =
𝐴 + 𝐵 𝐶𝐷
Vs
Vs
Vs

## Slide 28: Practice Problem 2
Design a circuit using ideal MOSFETs (S-model) to implement the logic function
[De Morgan’s Theorem]

## Slide 29
Practice Problem 1
In digital systems, binary data may be subjected to noise that can alter a 0 to a 1 or a 1 to a 0.
A simple way to check if any error has occurred is to use an even parity checker. If there are two input bits and , the output of the even parity checker (denoted as ) will be HIGH if there are even number of 1s, i.e., if both x and y are 0 or if both of them are 1.
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 30: Voltage Transfer Characteristics (VTC)
Reminder: VTC is a graph where axis = input voltage, -axis = output voltage
Why? Design logic gates to follow a given static discipline
When (Logical 0) (Logical 1)
When (Logical 1) (Logical 0)

## Slide 31: VTC of NAND gate
When
When
We only have one axis, but two inputs
Solution: Draw two VTC, one considering one considering

## Slide 32: VTC of NAND gate
𝑉Y = 0
𝑉Y = 1
Homework: Find VTC for NOR gate
When
When
We only have one axis, but two inputs
Solution: Draw two VTC, one considering one considering

## Slide 33: Outline
Constructing a *real* MOSFET – n/p-channel
Operation of an MOSFET-
  Cut-Off
  Saturation
  Triode Mode
Output Characteristics
PWL Model and Non-ideal Analysis: SR model
Real MOSFET equations
Introduction to Static analysis

## Slide 34: Construction of Real MOSFET
100
𝜇𝑚
Top view of several n-channel MOSFETs fabricated on a chip. The square MOSFETs in the center of the photograph have a width and length of 100 μm. (Photograph Courtesy of Maxim Integrated Products.)

## Slide 35: Real MOSFET – Enhancement Type
Device Structure (n-channel MOSFET)

## Slide 36: n-channel MOSFET (NMOS) Physical Structure
n-type
metal
metal
oxide insulator
metal
p-type
metal
gate
source
drain
n-type
e
e
e
e
e
e
h
h
h
h
h
h
Enhancement Type

## Slide 37: NMOS in Equilibrium
When the transistor is left alone, some electrons from the n-type wells diffuse into the p-type material to fill holes.
This creates negative ions in the p-type material and positive ions are left behind in the n-type material.
n-type
metal
metal
oxide insulator
metal
p-type
metal
gate
source
drain
n-type
+
+
+
+
+
+
_
_
_
_
_
_
h
h
h
h

## Slide 38: NMOS in Cutoff
When a small, positive VGS is applied, holes “move away” from the gate.
Electrons from complete atoms elsewhere in the p-type material move to fill holes near the gate instead.
n-type
metal
metal
oxide insulator
metal
p-type
metal
gate
source
drain
n-type
+
+
+
+
+
+
_
_
_
_
_
_
h
h
h
h
-
+
_
_
_
h
VGS > 0

## Slide 39: NMOS Transistor channel
When VGS is larger than a threshold voltage VTH(n), the attraction to the gate is so great that free electrons collect there.
The applied VGS creates an induced n-type channel under the gate (an area with free electrons).
n-type
metal
metal
oxide insulator
metal
p-type
metal
gate
source
drain
n-type
+
+
+
+
+
+
_
_
_
_
_
_
h
h
h
h
-
+
_
_
_
h
VGS > VTH(n)
h
h
h
h
h
e
e
e
e
e

## Slide 40: NMOS Transistor Drain Current
When a positive VDS is applied, the free electrons flow from the source to the drain. (Positive current flows from drain to source).
The amount of current depends on VDS, as well as the number of electrons in the channel, channel dimensions, and material.
n-type
metal
metal
oxide insulator
metal
p-type
metal
gate
source
drain
n-type
+
+
+
+
+
+
_
_
_
_
_
h
h
h
h
-
+
h
VGS > VTH(n)
h
h
h
h
h
-
+
VDS > 0
_
_
_
_
e
e
e
e
e

## Slide 41: NMOS Transistor Circuit symbol
n-type
metal
metal
oxide insulator
metal
p-type
metal
gate
source
drain
n-type
-
+
VGS
-
+
VDS
ID
IG
G
D
S
ID
IG
- VDS +
+
VGS
_

## Slide 42: NMOS I-V Characteristic
G
D
S
ID
IG
- VDS +
+
VGS
_
Since the transistor is a 3-terminal device, there is no single I-V characteristic.
Note that because of the insulator, IG = 0 A.
We typically define the MOS I-V characteristic as
ID vs. VDS for a fixed VGS.
The I-V characteristic changes as VGS changes.

## Slide 43: Modes of Operation
For small values of VGS, VGS ≤ VTH(n), the n-type channel is not formed. No current flows. This is cutoff mode.
When VGS > VTH(n), current ID may flow from drain to source, and the following modes of current flow are possible.
  The mode of current flow depends on the propelling voltage, VDS, and the channel-inducing voltage,
  VGS – VTH(n).
  When VDS < VGS – VTH(n), current is starting to flow. ID increases rapidly with increased VDS. This is triode mode.
  When VDS ≥ VGS – VTH(n), current is reaching its maximum value. ID does not increase much with increased VDS. This is called saturation mode.

## Slide 44: Water Tap Analogy
Imagine the water tap on your kitchen sink.
To make water flow, the water supply has to be connected to the water tap. This establishes a path for water to flow.
Setting VGS above the threshold voltage is like connecting the water supply.
Cutoff = water supply disconnected (no path for current flow)
Setting VGS to a larger value is like connecting a high-pressure water supply—more flow can potentially occur.

## Slide 45: Water Tap Analogy
The water tap itself is used to adjust water flow. You can turn the flow up and down.
VDS is like the water tap. It controls the amount of flow.
There is, of course, a saturation point. If you keep turning the water tap control, eventually you won’t get any more flow.
Triode = water tap in “normal range”, controls flow
Saturation = water tap turned up to (or past) point for maximum flow

## Slide 46: NMOS Equations
Cutoff Mode
Occurs when
Triode Mode
Occurs when and
Saturation Mode
Occurs when and
: Overdrive Voltage
The minimum voltage necessary at the gate terminal to form a channel.
Indicates the available excess voltage at gate after forming the n-channel.

## Slide 47: Real MOSFET
: Gate Voltage
Drain to Source Voltage
: Threshold Voltage
Overdrive voltage
MOSFET transconductance

## Slide 48: NMOS Triode Mode
Occurs when and
In triode mode, average voltage across channel is actually:
()
Overdrive Voltage is defined as:

## Slide 49: NMOS Saturation mode
Overdrive Voltage is defined as:
Occurs when and
In Saturation mode, average voltage across channel fixed at:

## Slide 50: Solving Circuits with MOSFET
Use Method of Assumed State!
Three steps:
  Assume: One of the modes (Cutoff, Triode, Saturation)
  Solve: Use corresponding equation and KCL+KVL
  Verify: Check if the conditions of and are satisfied. If not, repeat.
Might need to solve quadratic equation (𝑎𝑥2 + 𝑏𝑥 + 𝑐 = 0).
If we get two roots, choose the one that’s favorable to your assumption

## Slide 51: Example 1
Analyze the circuit to find and using the Method of Assumed State. Here, the input of the MOSFET is . You must validate your assumptions.
Assume:
  Let MOSFET be in Saturation mode:
  or
Solve:
Current Equation:
Verify: For Saturation mode
But here,
Here, the conditions are NOT fulfilled.
Assumption is INCORRECT!

## Slide 52: Example 1
Analyze the circuit to find and using the Method of Assumed State. Here, the input of the MOSFET is . You must validate your assumptions.
MOSFET is in Triode Mode.
or

## Slide 53: Example 2
Design the circuit, that is, determine the values of and , so that the transistor operates at and . The NMOS transistor has , .
Assume:
  Let MOSFET be in Saturation mode:
Solve:
Current Equation:
or

## Slide 54: Example 2
Design the circuit, that is, determine the values of and , so that the transistor operates at and . The NMOS transistor has , .
Verify:
Clearly
Assumption is CORRECT!

## Slide 55: Example - 3
For the circuit, find the value of that results in . The MOSFET has , ,
Assume:
  Let MOSFET be IS in Saturation mode:
Proof:
  Saturation Mode
Solve:
Current Equation:

## Slide 56: Example - 4

## Slide 57: Example - 4
Assume:
  Let MOSFET be in Saturation mode:
Solve:
Current Equation:
or

## Slide 58: Example - 4
Verify:
For Saturation mode
Assumption is CORRECT!

## Slide 59
Example - 5
Solve:
  Both MOSFET are in SATURATION:
  Q1:
  Q2:
Current Equation:

## Slide 60
Example - 5
Solve:
or

## Slide 61: NMOS I-V Characteristic
vs
When :
  for any

## Slide 62: NMOS I-V Characteristic
triode mode
cutoff mode (when VGS < VTH(N))
saturation mode
VDS
ID
VGS = 3 V
VGS = 2 V
VGS = 1 V
VDS = VGS - VT

## Slide 63: n-channel MOSFET - Summary
G – Gate: Trigger terminal
S – Source: Charge carrier reservoir
D – Drain: Charge carrier sink
No channel, open ckt
The created channel will have some R
-> SR model
Small Triode Mode
Large Saturation Mode
Cut off mode

## Slide 64: n-channel MOSFET - Summary
SR model is a better approximation than S model.
Triode Mode exists until: <=
Indicates the available excess voltage at gate after forming the n-channel.
SR Model:

## Slide 65: SR Model - Inverter
Vss
Vss
Vss
Vss
For example, If

## Slide 66: Design of logic gates
𝐵
𝐼𝑁 | 𝑩 | 𝑶𝑼𝑻
Low ( | High (5𝑉) | Low ()
High ( | Low | High (5V)
𝐼𝑁 | 𝑩 | 𝑶𝑼𝑻
 | High (5𝑉) | 
 |  | High (5V)
𝐼𝑁 | 𝑩 | 𝑶𝑼𝑻
Low | High (5𝑉) | Low ()
High ( |  | Low()
𝐼𝑁 | 𝑩 | 𝑶𝑼𝑻
 | High (5𝑉) | 
Expected
Actual
Therefore, need to design logic gates properly such that

## Slide 67: Design of logic gates - Example
Solution:
Now,
Hence
Assume the following values for the inverter circuit parameters: and Assume, further, that for the MOSFET. Determine a sizing for the MOSFET so that the inverter gate output for a logical 0 is able to switch OFF the MOSFET of another inverter.
[Assume if is not given or low]

## Slide 68: Review – MOSFET
Control controls the IV between drain-source ( vs )
Threshold voltage = 𝑉T, minimum voltage required to create the channel
Models
S Mode: Assumes an ideal channel with zero resistance
SR Model: Assumes finite channel resistance, depends on

## Slide 69: NMOS Triode Mode
For small

## Slide 70: MOSFET Linear Models
S Model
SR Model

## Slide 71: Construction of Real MOSFET
Simplified cross section and 3D view
12
𝑉 = 0𝑉
12
𝑉 > 𝑉
$
No channel, open ckt
Channel created Will have some R
-> SR model

## Slide 72: Real MOSFET
For small uniform channel, hence fixed therefore SR model valid.
As is increased, channel becomes tapered cause ↓. Resistance ↑, slope ↓.
This mode is called the triode mode. Condition:

## Slide 73: Real MOSFET
When , channel pinches off.
Increasing further have no effect on channel shape. Hence, current saturates
This mode is called the saturation mode. Condition:
Behaves like a current source (constant current) that depends on '

## Slide 74: IV Characteristics of Real MOSFET
Mode | Condition | Equation
Cutoff | 𝑉%& < 𝑉' | 𝐼) = 0
Triode | 𝑉%& ≥ 𝑉' 𝑉)& < 𝑉!( | 𝐼 = 𝑘[𝑉 𝑉 − 1 𝑉* ] ) !( )& 2 )&
Saturation | 𝑉%& ≥ 𝑉' 𝑉)& ≥ 𝑉!( | 𝐼 = 𝑘 𝑉* ) 2 !(